## Slide 1
Measurement Simulation
Using SA to plan your work
Steve Seiler
Scott Sandwith

## Slide 2
Topics
01. Instrument Uncertainty Parameters Where they are and how to change.
02. Effect of Instrument Uncertainty
Points from 1 instrument and composite points.
03. Job Planning
Where to set up? How many instruments are needed? Can desired uncertainty be achieved?

## Slide 3
Instrument
Uncertainty Parameters
Laser Trackers, Total Stations and Laser Radar
Horizontal
Vertical
Distance
Notes: Instrument Properties > Edit Uncertainty Variables
Trackers, Total Stations and Laser Radar have angular and distance uncertainty components.

## Slide 4
Instrument
Uncertainty Parameters
Theodolites
Horizontal
Vertical
Notes: Instrument Properties > Edit Uncertainty Variables
Theodolites have only 2 angular components; they cannot measure distance.

## Slide 5
Instrument
Uncertainty Parameters
PCMM Arms
6 or 7 encoder angular uncertainties
Notes: Instrument Properties > Edit Uncertainty Variables
Arms have uncertainty values given to each encoder.

## Slide 6
Effect of
Instrument Uncertainty
Notes: Changing the uncertainty parameters of an instrument will change the shape of the resulting uncertainty field of points subsequently measured by that instrument.

## Slide 7
Effect of
Instrument Positions
Given:
Find:
8m x 8m x 4m work volume
20m distance from instrument to center of work volume
-3 instrument configuration to find the lowest uncertainty at the center of the volume
Notes: How should I arrange my instruments to get the best overall uncertainty at the center of my work volume?

## Slide 8
Effect of
Instrument Positions
 |  | 2σ Uncertainty |  |  |  | % Improvement |  |  | 
 | Instrument Configuration | Ux | Uy | Uz | Mag | Ux | Uy | Uz | Mag
 |  | (mm) | (mm) | (mm) | (mm) | % | % | % | %
5 m | 3 Near Setups | 0.023 | 0.028 | 0.029 | 0.046 |  |  |  | 
 | 3 Varied Setups | 0.025 | 0.025 | 0.029 | 0.046 | -10 | 10 | -2 | 0
 | Best Case | 0.026 | 0.026 | 0.026 | 0.045 | -15 | 7 | 8 | 2
20 m | 3 Near Setups | 0.066 | 0.108 | 0.109 | 0.167 |  |  |  | 
 | 3 Varied Setups | 0.077 | 0.086 | 0.107 | 0.157 | -16 | 20 | 2 | 6
 | Best Case | 0.090 | 0.088 | 0.090 | 0.155 | -37 | 19 | 17 | 7
40 m | 3 Near Setups | 0.126 | 0.223 | 0.224 | 0.340 |  |  |  | 
 | 3 Varied Setups | 0.151 | 0.164 | 0.207 | 0.304 | -20 | 26 | 7 | 10
 | Best Case | 0.167 | 0.166 | 0.167 | 0.288 | -33 | 26 | 25 | 15
Notes: The instrument configuration has more influence on the resulting uncertainty the further the instruments are from the center of the work volume. If you only care about one coordinate direction, you should have a different strategy for configuring the instruments than if all directions are equally as important.

## Slide 9
Job Planning Demo
Measure this…
Knowing this is in the way…
Find Expected:
-Focal Length Uncertainty
-Paraboloid Axis Uncertainty
-# and location of instruments
to achieve these

## Slide 10
USMN for
Job Planning

## Slide 11
Job Planning Demo
Results
2σ Uncertainties with 300 samples |  |  |  |  |  |  |  |  |  |  |  | 
 | # Inst | # Paraboloid Points | Inst. Index |  |  |  | Focal Length (in) | Focal Length Unc. (in) | Paraboloid Axis Unc. (Deg) |  |  | 
 | 2 | 17 | X | X |  |  | 93.0076 | 0.0138 | 0.0757 |  |  | 
 |  | 16 | X |  | X |  | 93.0033 | 0.0117 | 0.0630 |  | Length | Axis
 |  | 15 | X |  |  | X | 92.9874 | 0.0207 | 0.0952 |  | 0.0100 | 0.06
 |  | 17 |  | X | X |  | 93.0050 | 0.0130 | 0.0714 |  |  | 
 |  | 15 |  |  | X | X | 93.0038 | 0.0102 | 0.0612 |  | 0.0125 | 0.07
 |  | 17 |  | X |  | X | 92.9981 | 0.0129 | 0.0816 |  |  | 
 | 3 | 18 | X | X | X |  | 92.9932 | 0.0107 | 0.0546 |  |  | 
 |  | 18 | X | X |  | X | 92.9907 | 0.0116 | 0.0624 |  |  | 
 |  | 16 | X |  | X | X | 93.0011 | 0.0101 | 0.0558 |  |  | 
 |  | 18 |  | X | X | X | 93.0055 | 0.0107 | 0.0592 |  |  | 
 | 4 | 18 | X | X | X | X | 93.0016 | 0.0089 | 0.0463 |  |  | 
Best Choice 2 LT
Best Choice 3 LT
Only Choice for Goal Unc.
Goal Uncertainty

## Slide 12
THANK YOU