## Slide 1: GD&T Inspection
Jeremy Winn
Support AE
Williamsburg, VA
Zach Rogers
Application Engineer
Germany

## Slide 2: What is “GD&T” in the SA world?
Incorporating
Standardized Inspection within SpatialAnalyzer
ASME 1994 Foundation
ASME is a single standard with a thorough explanation and complimentary examples. It is also revised infrequently providing consistency.
Validation for both ASME and ISO is provided.

## Slide 3: GD&T Inspection
GD&T
“Regular Inspection”
Alignments:
Datum Structure
User Choice…
Notes: SA’s GD&T Inspection tools provides engineer’s the ability to perform standardized Geometric Dimensioning and Tolerancing
with complete confidence that their inspection is in accordance with the guidelines of the ASME or ISO standard.

## Slide 4: GD&T Inspection
GD&T
“Regular Inspection”
User Choice…
Datum Structure
Bounding Condition***
RMS (root mean square)
Alignments:
Evaluation:
Notes: SA’s GD&T Inspection tools provides engineer’s the ability to perform standardized Geometric Dimensioning and Tolerancing
with complete confidence that their inspection is in accordance with the guidelines of the ASME or ISO standard.

## Slide 5: GD&T Inspection
GD&T
“Regular Inspection”
Alignments:
User Choice…
Datum Structure
Evaluation:
Bounding Condition***
RMS (root mean square)
Goal:
Pass / Fail Result
Understand Contributing errors
Notes: SA’s GD&T Inspection tools provides engineer’s the ability to perform standardized Geometric Dimensioning and Tolerancing
with complete confidence that their inspection is in accordance with the guidelines of the ASME or ISO standard.

## Slide 6: GD&T Inspection
GD&T Inspection - 2 Distinct Steps
2. Measurement Process
  Data Gathering & Association
    Inspection/ inspect scripting
    Toolkit or direction Association
    or Measurement Plan (MP)
1. Defining the Checks
Building Annotations
    Tolerance Structure
    Nominal designation

## Slide 7: Building Annotations
The Definition and Details for a Check.

## Slide 8: GD&T Annotations
First Option - Import
Importing from CAD:

## Slide 9
GD&T Annotations
Anatomy of an Annotation
Surface Profile
Tolerance = 0.012
With an Alignment:
Primary Datum A
Secondary Datum B
Tertiary Datum C

## Slide 10
GD&T Annotations
Anatomy of an Annotation

## Slide 11: GD&T Annotations
Anatomy of an Annotation
SA Objects/CAD Face
Datum Assignment
Tolerance Definition

## Slide 12
Building Annotations

## Slide 13: GD&T Annotations
Annotation View Orientation:

## Slide 14: GD&T Annotations
Datum and Datum Target Designations
    (Hold down A-Z to pick a letter)
    Click-point defines leader line anchor point

## Slide 15: GD&T Annotations
Feature Checks Designation:
1.
2.
3.

## Slide 16: GD&T Annotations
Anatomy of an Annotation
New Right-Click Options:
Annotation Notes
Drag Annotations
Set Text Scale
Show/Hide Selected
Callout Views & Layers

## Slide 17: GD&T Inspection
GD&T Inspection - 2 Distinct Steps
2. Measurement Process
  Data Gathering & Association
    Inspection/ inspect scripting
    Toolkit or direction Association
    or Measurement Plan (MP)
1. Defining the Checks
Building Annotations
    Tolerance Structure
    Nominal designation

## Slide 18: GD&T Inspection
Tree Structure
  Annotations
    Tolerance & check definition
  Datums & Feature Checks
    Link points to annotations
    Point offset & evaluation control
    Contain guided inspection controls
Inspections must be in the working collection and are collection specific.

## Slide 19: GD&T Inspection
Direct Point Association

## Slide 20: GD&T Inspection
Trapping Measurements

## Slide 21: GD&T Inspection
Guided Inspection

## Slide 22
Demo – Basic Fit & Link Data

## Slide 23
Automatic Point Association
GD&T Inspection
Things to remember:
Proximity Filter
Based on Initial
Alignment

## Slide 24
Automatic Point Association
GD&T Inspection

## Slide 25
Automatic Point Association
GD&T Inspection

## Slide 26: Working Without CAD
Remember your basics

## Slide 27: GD&T Inspection

## Slide 28: GD&T Inspection

## Slide 29: GD&T Inspection
GD&T Inspection - 2 Distinct Steps
1. Defining the Checks
Building Annotations
    Tolerance Structure
    Nominal designation

## Slide 30: GD&T Inspection

## Slide 31: GD&T Inspection

## Slide 32: Report Options

## Slide 33: Reporting

## Slide 34: Reporting
Basic Report Display Options
Measured Deviation (GD&T Result)
Distance Out of Tolerance
Reports the Worse Value

## Slide 35: Reporting
Basic Report Display Options
Measured Deviation (GD&T Result)
Distance Out of Tolerance
Alignment Transform
Datum Deviations Statistics

## Slide 36: Reporting
Basic Report Display Options
Bonus Tolerance Information
Pattern Feature Deviation
Position and Profile Only

## Slide 37: Reporting
Basic Report Display Options

## Slide 38: Getting into the Details
Understanding Check Types

## Slide 39: GD&T Annotations
  Form Checks
    Datum Independent
Feature Checks Designation:

## Slide 40: Flatness
Standard Inspection (RMS):

## Slide 41: Flatness
Flatness Evaluation Process within SA:
Two parallel planes are built bounding the extents of the data.
These planes are allowed to freely rotate to establish the minimum distance between them while still containing the data.

## Slide 42: GD&T Annotations
  Form Checks
    Datum Independent
  Orientation Checks
    Depend on 1 Datum
Feature Checks Designation:

## Slide 43: Orientation Checks
Datum
Nominal Angle
Deviation = Distance btw Planes

## Slide 44: GD&T Annotations
  Form Checks
    Datum Independent
  Orientation Checks
    Depend on 1 Datum
  Location Checks
    Can Include 1-3 Datums
    Can Include 1-2 Tiers
Feature Checks Designation:

## Slide 45: GD&T Annotations
Surface Profile:
GD&T Reports:
Measured Deviation (GD&T Result)
Distance Out of Tolerance
Vectors Report:
Radial Deviation
Distance out of Tolerance

## Slide 46: GD&T Annotations
Composite True Position:

## Slide 47
GD&T Annotations
Dimensional Tolerances
Notes: Feature Check selection simplifies check assocation

## Slide 48
GD&T Annotations
Dimensional Tolerances

## Slide 49: GD&T Annotations
Feature Checks Categories:
Cross Section
Checks

## Slide 50: GD&T Annotations
Cross Section Checks:
Runout
Cross Section
Check
Total Runout
Surface Check

## Slide 51: GD&T Annotations
Cross Section
Checks

## Slide 52: Feature Check Properties
Going a Bit Deeper

## Slide 53
Building Feature Checks
Inspection Controls
Evaluation Method
Offset Compensation

## Slide 54: Building Feature Checks
Cylinder Evaluation Method
Circle Fit Evaluations:
Axis Fit Evaluations:

## Slide 55: Building Feature Checks
Cylinder Evaluation Method
Extrapolate Axial Extents
Off…

## Slide 56: Building Feature Checks
Cylinder Evaluation Method

## Slide 57: Datum Alignment

## Slide 58: Datum Alignment
Right- Click Datum Category
  Select “Align”

## Slide 59: Datum Alignment
Datums and Degrees of Freedom
Geometry Type
Sequence
3 DoF Remain
Rx, Ry, Z
A
Rx, Ry, Z + X, Rz
1 DoF Remains
B
X,Z, Rx, Ry, Rz + Y
C

## Slide 60: Datum Alignment
Datums and Degrees of Freedom
Geometry Type
Sequence
1 DoF Remains
Rx, Ry, Z + X, Y
Rx, Ry, Z
3 DoF Remain
A
B
X,Y,Z, Rx,Ry, + Rz
C

## Slide 61
Offset Compensation
Datum Alignment

## Slide 62
Datum Alignment
Enable Datum Alignment

## Slide 63: Datum Alignment
Aligning to Curved Surfaces
Surface Datums require “Offset Object” designation
Constrains (Rx, Ry, Z )
but not (Rz, X or Y)
Constrains (X,Z,Rx,Rz )
but not (Y or Ry)

## Slide 64: Datum Alignment
Aligning to Curved Surfaces
Surface Datums require “Offset Object” designation

## Slide 65: Datum Alignment
Aligning to Curved Surfaces

## Slide 66: Evaluations Tools

## Slide 67: Questions?

## Slide 73: Troubleshooting
Check Computation
Geom Relationships
Datum Alignment
Curvy Surfaces

## Slide 74: Demo- Basic Fit & Link
Notes: Objective is to demonstrate:
Setting a view for the Annotations
Adding Datums Annotations
Adding Feature checks Annotations
Opening the Properties and changing properties
Controlling Graphical Placement
End with Direct CAD Import with all the annnotations

## Slide 75: Reporting
Basic Report Display Options

## Slide 76: Reporting
Basic Report Display Options

## Slide 77: Reporting
Inspection
Controls

## Slide 78: Reporting
Callout layer control now supports Annotations

## Slide 79: Datum Alignment
Start thinking:
Datum Priority
Degrees of Freedom
Offset Compensation
Z,Rx,Ry
X,Y,Z
X,Y,Rx,Ry
X,Y,Z,Rx,Ry
X,Y,Z,Rx,Ry,Rz
All 6 DoF are constrained with 1 datum…

## Slide 80: Concentricity
Cross Section Checks:
Concentricity
Cross Section
Check

## Slide 81: GD&T Inspection
Why GD&T???
GD&T answers the following questions:
1. How did you align to the part?
2. What evaluation method did you use?
3. What tolerance did you use?
Will the bolt fit in the hole, YES or NO?
Notes: SA’s GD&T Inspection tools provides engineer’s the ability to perform standardized Geometric Dimensioning and Tolerancing
with complete confidence that their inspection is in accordance with the guidelines of the ASME or ISO standard.

## Slide 82: GD&T Annotations
Datum and Datum Target Designations
    (Hold down A-Z to pick a letter)
    Click-point defines leader line anchor point

## Slide 83: Building Annotations Demo
Notes: Objective is to demonstrate:
Setting a view for the Annotations
Adding Datums Annotations
Adding Feature checks Annotations
Opening the Properties and changing properties
Controlling Graphical Placement
End with Direct CAD Import with all the annnotations

## Slide 84: Associating Data
Working with Datums and Feature Checks