## Slide 1: SA Robot Calibration Appliance Workshop
By: Sandwith

## Slide 2: What can SARCA do?
Solve as-built kinematic model of a robot in cell
Solve robot base coordinate system
Solve for As-built TCP offset
Calibrate a robot in specific zones
Compensate for Robot deflection loads
Compensate for joint backlash
Compensate gravitational deflection
Used with native robot language

## Slide 3: Advantages of SARCA
Supports Kuka, ABB, FANUC, Comau
Robot accuracy performance improvement
Enhanced robot kinematic model
Multiple Zone and Load Calibrations available at Run Time
Native Robot language access to SARCA calibration can be used to write motion programs
SARCA calibration do not require metrology in production
Metrology system could be used for several robots at the same time
3 Reflectors can be used for 6DoF measurements

## Slide 4: Accurate SARCA Applications
Medical Patient Positioning
Accurate Determinate Assembly Drilling
Accurate Torch Cutting Paths

## Slide 5: How does it work?
Application Computer
Running SA
Robot
Controller
Laser Tracker Controller ATC
LAN (RJ45)
LAN (RJ45)
LAN (RJ45)
Embedded
SARCA
Controller

## Slide 6: Calibration Appliance Process Flowchart
Inputs:
  Set CalibrationID
  Program Poses (Zone)
  Interface Metrology System
Run Robot Cal Program
Solve / Accept Cal
Output: As-Built Kinematic Models

## Slide 7: Architecture
Production Run Configuration Schematic

## Slide 8: Calibrated Robot Production Run Flowchart
Program Robot (Native Language)
  Run – Select CalibrationID
  Retrieve Cal Base and Tool
  For each Point(i)
    Inverse Kinematics
    Compute Accurate Joint Angles
    Forward Kinematics
  Point(i’) [Calibrated]

## Slide 9: Calibration Appliance Communication

## Slide 10
Acquire measurement data
Measure n – 6DoF positions distributed over the work space of the robot..
Calibration Process

## Slide 11
Calibration Process – SA Machine

## Slide 12
Extrinsic Calibration Cell Alignment
Notes: Identify robot base coordinate system relative to tracker and tool system

## Slide 13
Base Offset
Calculate base offset by fixing all other parameters
Extrinsic Calibration

## Slide 14
Optimize Physical Parameters
Optimize geometric parameters (Denavitt Hartenberg parameters)
Intrinsic Calibration
Notes: Normally (DH-Parameter identification):
Newton-Gauss Algorithm
Levenberg-Marquardt Algorithm
We have our own specialized algorithms

## Slide 15
Zone Specific Calibration
Zone 1
Zone 2
Zone 3
Notes: Advantage of this method, zone specific calibration is very easy

## Slide 16
Compliance Model Identification
Extract weights and centers of gravity from CAD data
Elasticity Calibration

## Slide 17
Compliance Model Identification
Extract weights and centers of gravity from CAD data
Elasticity Calibration

## Slide 18
Gravitation Settings
Define gravity relative to active base frame
Elasticity Calibration

## Slide 19
Calibrate for Different Load Cases
Attach different tool loads and repeat the calibration process in order to obtain a compound calibration
Tool Loads

## Slide 20
Tool Loads
5 kg
10 kg
20 kg

## Slide 21
Backlash Identification
Empirically determined by measurement or configured based on specifications
Backlash Compensation

## Slide 22
Evaluate Calibration Results
The nearer to zero the better
Solution RMS, Robustness

## Slide 23: Calibration Appliance Communication
Application Computer
Running SA
Robot
Controller
Laser Tracker Controller ATC
LAN (RJ45)
LAN (RJ45)
LAN (RJ45)
Embedded
SARCA
Controller

## Slide 24: Calibration Appliance Process Flowchart
Inputs:
  Set CalibrationID
  Program Poses (Zone)
  Interface Metrology System
Run Robot Cal Program
Solve / Accept Cal
Output: As-Built Kinematic Models

## Slide 25: Architecture
Production Run Configuration Schematic

## Slide 26: Calibrated Robot Production Run Flowchart
Program Robot (Native Language)
  Run – Select CalibrationID
  Retrieve Cal Base and Tool
  For each Point(i)
    Inverse Kinematics
    Compute Accurate Joint Angles
    Forward Kinematics
  Point(i’) [Calibrated]

## Slide 27: Calibration Appliance Communication

## Slide 28: Test Setup
ABB 6640
Leica AT-901 + T-MAC
SARCA
Network Switch

## Slide 29: Test Setup
Test Volume: 80” x 40” x 40”

## Slide 30: AbsAcc v. SARCA Validation Errors
AbsAcc Errors (x 1000)
SARCA Errors (x 1000)
Test Volume: 80” x 40” x 40”
Max: 0.046” Avg: 0.025
Max: 0.009” Avg: 0.005

## Slide 31: Test Results
Analysis comparison (inches) programming to the work object (2 m x 1 m x 1 m).
 | SARCA | AbsAcc
Min | 0.001 | 0.008
Max | 0.009 | 0.046
Average | 0.005 | 0.025
StdDev from Avg | 0.002 | 0.009
StdDev from Zero | 0.005 | 0.027
RMS | 0.005 | 0.027

## Slide 32: Test Results
AbsAcc Results
SARCA Results